## Slide 1: The parts
Windows icon tray
Hardware
"TotalMix" control software
Hardware config panel

## Slide 2: The 18 hardware inputs
AN 1
Mic/Line 1
AN 2
Mic/Line 2
XLR connector: mic with pre-amp
(Phantom pwer is enabled in TotalMix)
Jack plug: line
AN 3 AN 4
Line inputs
AN 8 AN 7 AN 6 AN 5
More ANalog line inputs
SPDIF 9-10
digital, stereo
2
ADAT 11-18
optical link, 8 channels
8
(In SuperCollider and FonaDyn, these are numbered 0…17.)

## Slide 3: The 18 hardware outputs
AN 7-8
analog, stereo
headphones or line output
2
ADAT 11-18
optical link, 8 channels
8
AN 6 AN 5 AN 4 AN 3 AN 2 AN 1
ANalog line outputs
SPDIF 9-10
digital, stereo
2
(In SuperCollider and FonaDyn, these are numbered 0…17.)

## Slide 4: Signal flow
Hardware inputs
(18 sliders top row)
Hardware outputs
(18 sliders bottom row)
Each output gets its own mix of up to 18+18 inputs
All computer apps
with record and/or play
18 fixed gain
Choose record device in the app
Software playback
(18 sliders middle row)
Choose playback device in the app

## Slide 5: TotalMix signal flow
Hardware inputs
Hardware outputs
Audio software apps
Record Play
HARDWARE INPUTS
top row
middle row
SOFTWARE PLAYBACK
HARDWARE OUTPUTS
bottom row
mixing

## Slide 6: From the UCX manual
record
record